## Slide 1: P&S Modern SSDs Basics of NAND Flash-Based SSDs
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
12 October 2022

## Slide 2: Today’s Agenda
SSD Organization & Request Handling
NAND Flash Organization
SSD Organization & Request Handling
NAND Flash Organization

## Slide 3: Modern SSD Architecture
A modern SSD is a complicated system that consists of multiple cores, HW controllers, DRAM, and NAND flash memory packages
Samsung PM853T 960GB Enterprise SSD (from https://www.tweaktown.com/reviews/6695/samsung-pm853t-960gb-enterprise-ssd-review/index.html)
Core
Core
Core
HW
Flash Ctrl.
HW
Flash Ctrl.
HW
Flash Ctrl.
HW
Flash Ctrl.
Request Handler
ECC/Randomizer
Encryption Engine
SSD Controller
NAND Packages
8×128 GB = 1 TB
LPDDR DRAM
0.001×1,024 = 1 GB

## Slide 4
Another Overview
Host Interface Layer (HIL)
Flash Translation Layer (FTL)
Data Cache Management
Address Translation
GC/WL/Refresh/…
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Host Request Queue
Write Buffer
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
4

## Slide 5
Flash Translation Layer (FTL)
Request Handling: Write
Data Cache Management
Address Translation
GC/WL/Refresh/…
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
Host Interface Layer (HIL)
DRAM
Write Buffer
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Host Request Queue
Communication with the host operating system (receives & returns requests)
  Via a certain interface (SATA or NVMe)
A host I/O request includes
  Request direction (read or write)
  Offset (start sector address)
  Size (number of sectors)
  Typically aligned by 4 KiB
5

## Slide 6
Host Interface Layer (HIL)
Request Handling: Write
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Host Request Queue
Buffering data to write (read from NAND flash memory)
  Essential to reducing write latency
  Enables flexible I/O scheduling
  Helpful for improving lifetime (not so likely)
Limited size (e.g., tens of MBs)
  Needs to ensure data integrity even under sudden power-off
  Most DRAM capacity is used for L2P mappings
Flash Translation Layer (FTL)
Address Translation
GC/WL/Refresh/…
Write Buffer
Data Cache Management
6

## Slide 7
Host Interface Layer (HIL)
Request Handling: Write
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Metadata (e.g., P/E Cycles)
Host Request Queue
Core functionality for out-of-place writes
  To hide the erase-before-write property
Needs to maintain L2P mappings
  Logical Page Address (LPA)  Physical Page Address (PPA)
Mapping granularity: 4 KiB
  4 Bytes for 4 KiB  0.1% of SSD capacity
Flash Translation Layer (FTL)
GC/WL/Refresh/…
Write Buffer
Data Cache Management
Address Translation
Logical-to-Physical Mappings
7

## Slide 8
Host Interface Layer (HIL)
Request Handling: Write
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Host Request Queue
Garbage collection (GC)
  Reclaims free pages
  Selects a victim block  copies all valid pages  erase the victim block
Wear-leveling (WL)
  Evenly distributes P/E cycles across NAND flash blocks
  Hot/cold swapping
Data refresh
  Refresh pages with long retention ages
Flash Translation Layer (FTL)
Write Buffer
Data Cache Management
Address Translation
Logical-to-Physical Mappings
GC/WL/Refresh/…
Metadata (e.g., P/E Cycles)
8

## Slide 9
DRAM
Host Request Queue
Write Buffer
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Flash Translation Layer (FTL)
Data Cache Management
Address Translation
GC/WL/Refresh/…
Host Interface Layer (HIL)
Request Handling: Write
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
Randomizer
  Scrambling data to write
  To avoid worst-case data patterns that can lead to significant errors
Error-correcting codes (ECC)
  Can detect/correct errors: e.g., 72 bits/1 KiB error-correction capability
  Stores additional parity information together with raw data
Issues NAND flash commands
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
9

## Slide 10
Host Interface Layer (HIL)
Request Handling: Read
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Host Request Queue
First checks if the request data exists in the write buffer
  If so, returns the corresponding request immediately with the data
A host read request can be involved with several pages
  Such a request can be returned only after all the requested data is ready
Flash Translation Layer (FTL)
Address Translation
GC/WL/Refresh/…
Write Buffer
Data Cache Management
10

## Slide 11
Host Interface Layer (HIL)
Request Handling: Read
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Metadata (e.g., P/E Cycles)
Host Request Queue
Finds the PPA where the request data is stored from the L2P mapping table
Flash Translation Layer (FTL)
GC/WL/Refresh/…
Write Buffer
Data Cache Management
Address Translation
Logical-to-Physical Mappings
11

## Slide 12
DRAM
Host Request Queue
Write Buffer
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Flash Translation Layer (FTL)
Data Cache Management
Address Translation
GC/WL/Refresh/…
Host Interface Layer (HIL)
Request Handling: Read
First reads the raw data from the flash chip
Performs ECC decoding
Derandomizes the raw data
ECC decoding can fail
  Retries reading of the page w/ adjusted VREF
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
12
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
…

## Slide 13: Today’s Agenda
SSD Organization & Request Handling
NAND Flash Organization

## Slide 14: A Flash Cell
Basically, it is a transistor
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
ID
VTH
(Threshold Voltage)
VGS >VTH
VGS < VTH

## Slide 15: A Flash Cell
Basically, it is a transistor
  w/ a special material: Floating gate (2D) or Charge trap (3D)
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
VTH
FG
(Floating Gate)

## Slide 16: A Flash Cell
Basically, it is a transistor
  w/ a special material: Floating gate (2D) or Charge trap (3D)
  Can hold electrons in a non-volatile manner
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
VTH
FG
(Floating Gate)
VPGM = 20 V
GND
–
–
–
–
Tunneling

## Slide 17: A Flash Cell
Basically, it is a transistor
  w/ a special material: Floating gate (2D) or Charge trap (3D)
  Can hold electrons in a non-volatile manner
  Changes the cell’s threshold voltage (VTH)
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
VTH
FG
(Floating Gate)
VTH'
Tunneling
GND
20 V
–
–
–
–
VREF
VTH < VREF
VTH > VREF
‘1’
‘0’

## Slide 18: Flash Cell Characteristics
Multi-leveling: A flash cell can store multiple bits
Retention loss: A cell leaks electrons over time
Limited lifetime: A cell wears out after P/E cycling
Flash Cell
Program:
Inject electrons
Erase:
Eject electrons
11
01
00
10
2-bit Multi-level Cell
1 year
1 year
11
01
00
10
11
01
00
10
11
01
00
10
00
Retention error!
1 year
@ 1K P/E cycles
1 year
@ 10K P/E cycles
11
01
00
10
11
01
00
10
00
Retention error!
11
01
00
10

## Slide 19: A NAND String
Multiple (e.g., 128) flash cells are serially connected
…
Bitline (BL)
VPASS
(> 6V)
VPASS
VPASS
Target Cell
…
Bitline (BL)
NAND String

## Slide 20: Pages and Blocks
A large number (> 100,000) of cells operate concurrently
…
BL0
…
BL1
…
BL2
…
BL3
…
BL132,095
…
WL0
Wordline
WL1
WL126
WL127
…
…
…
…
Page = 16 + α KiB
Block = {(# of WL)×(# of bits per cell)} pages

## Slide 21: Pages and Blocks (Continued)
Program and erase: Unidirectional
  Programming a cell  Increasing the cell’s VTH
  Eraseing a cell  Decreasing the cell’s VTH
Programming a page cannot change ‘0’ cells to ‘1’ cells  Erase-before-write property
Erase unit: Block
  Increase erase bandwidth
  Makes in-place write on a page very inefficient  Out-of-place write & GC

## Slide 22: Planes
A large number (> 1,000) of blocks share bitlines in a plane
…
BL0
BL0
BL1
BL2
BL132,095
…
…
…
…
WL0
WL1
WL126
WL127
Block0
Block1
Block2
Block2,047
…

## Slide 23: Planes
A large number (> 1,000) of blocks share bitlines in a plane
…
BL0
WL0
WL1
WL126
WL127
SSL
GSL
String Select Line
Ground Select Line
BL0
BL1
BL2
BL132,095
…
…
…
…
Block0
Block1
Block2
Block2,047
…

## Slide 24: Planes and Dies
A die contains multiple (e.g., 2 – 4) planes
A 21-nm 2D NAND Flash Die
BL0
BL1
BL2
BL132,095
…
…
…
…
Block0
Block1
Block2
Block2,047
…
Plane1
Plane2
Plane3
Page Buffers
Peripheral Circuits
Row/Column Decoders
Plane0
Planes share decoders: limits internal parallelism (only operations @ the same WL offset)

## Slide 25: P&S Modern SSDs Basics of NAND Flash-Based SSDs
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
12 October 2022